## Slide 1: Delivering Cloud Ready Connectivity
Mark Vevers
Technical Design Authority
RM Education
rm.com/seminars

## Slide 2: Definition: What is ‘Cloud Ready’?
Cloud Ready …..
Not like ‘HD Ready’ TVs I promise!
Different scenarios
  Some services in the cloud – most local
  Hybrid model – 50% split
  100% cloud for Everything
rm.com/seminars

## Slide 3: Services to Consider
Admin / Business:
MIS
Email
Telephony (VoIP)
Building Management
CCTV / Alarm systems remote monitoring
Device management (MDM)
rm.com/seminars

## Slide 4: Services to Consider
Core Applications (inc Google G-Suite and Microsoft Office 365)
Other Apps – (e.g. RMEasimaths or Capita Reading Cloud)
Video
BYoD
Safeguarding – (filtering, logging, reporting, alerting)
Education
rm.com/seminars

## Slide 5: Supporting Services
Authentication / Authorisation & Accounting
AD? AD in the cloud?
Cloud Severs & Services
  Infrastructure as a Service (IaaS)
  Platform as a Service (e.g. MS SQL Database)
Backup
  Where is / will your data be?
rm.com/seminars

## Slide 6: Part 1: MUST HAVES
rm.com/seminars

## Slide 7: Part 1: What ‘Must’ your connection provide?
Bandwidth
Not just now– but three years time
  Always on, always the same – no ’peak’ slow downs
  Low latency / jitter
Stability
  Always there
  Resilience To Failure
  Resilience To Denial of Service
Availability
rm.com/seminars

## Slide 8: Bandwidth
We see: 30% Compound Annual Growth Rate
rm.com/seminars

## Slide 9: What is ‘Congestion’ and Why Does It Matter?
Network congestion:
    Packets arrive too fast at a router to fit in the outbound connection
    Packets are ‘buffered’ (think Tailback)
    But if too many arrive: Thrown Away!
  Impact:
    Audio or video ‘breaks up’
    Interactive applications become unresponsive
    Broken web-pages due to timeouts
rm.com/seminars

## Slide 10: Stability
Depends on connection type
Contention – effective vs actual
Technology type – all different: –
Leased line
FTTP
FTTC (VDSL)
4G (LTE)
Overload may occur outside your network/circuit
5G
rm.com/seminars

## Slide 11: 5G – to the Rescue?
Much hyped:
‘1ms Latency’
Performance
Coverage
Variability
Source: PCMag / Sascha Segan April 2019

## Slide 12: Latency, Jitter & Packet Loss
Latency (or PING times):
Round trip time of a packet between two devices
Increases with
Distance
Buffering
Jitter
Variable latency – mostly due to buffering on loaded connections
Packet Loss
Connection size
Processing capacity
rm.com/seminars

## Slide 13: Availability & Connection Failure
Link Down / Overloaded
DDoS’d?
No O365 / G-Suite cloud applications
Can’t access MIS
No phone / voice service
rm.com/seminars

## Slide 14: Availability Options – 1 : Full resilience
Idealised 100% Resilience
  Routers
  Fibre Paths
  Carriers & ISPs
  Different exchange/plant & equipment
Costly
  Financially
  Technically
  Operationally
rm.com/seminars

## Slide 15: Availability Options : 2 Backup FTTC circuit
Leased Line backed up by FTTC to same ISP
- Advantages
Much cheaper
Different access layer technology & plant
IP addressing, firewalling, access remain identical
=> Low financial, technical & operational overhead
Disadvantages
Bandwidth
Single points of failure
=> Balance of risk vs Benefit
rm.com/seminars
Notes: So perhaps a more realistic option which will meet the requirements of most
Backup circuit using a different technology to the same ISP
This allows you to move the ‘problem’ of resilience to your provider
But keep costs much more under control.
But with something like FTTC – bandwidth may not be

## Slide 16: Availability Options : 2 Backup FTTC circuit
Multiple
Connections
Routers
Switches
ISP Data Centres
Carriers ?
rm.com/seminars

## Slide 17: DDoS – Distributed Denial of Service
More than one type of attack
  Volumetric attack
  Resource consumption attack
Increasingly common
  Attacks mostly DURING term time!
  On-line ’booter’ services – often 5 mins for free
  Short but repeated & frequent
Can be > 800Gbit/s but usually at least 10 Gbit/s
  Specialist ‘tools’ / Services
rm.com/seminars

## Slide 18: How does DDoS Defence Work?
rm.com/seminars

## Slide 19: Part 1: Summary & Recommendations
Plan ahead at least three years for bandwidth utilisation
Avoided overloaded connections
But if using VoIP apply QoS to deal with ‘bursts’ anyway
Consider backup connections
Work out what you need to ‘survive’
Consider cost-benefit in detail
Connection technology IS important
5G Unlikely to be your saviour!
Usually 'cheapest'
rm.com/seminars

## Slide 20: Part 2: GREAT to HAVE
rm.com/seminars

## Slide 21: What ‘Could’ your connection provide?
Voice Services
Security
Intersite Connectivity
VPNs:
rm.com/seminars

## Slide 22: Voice Services
PSTN/ISDN Switch Off begins NEXT YEAR!
Voice over IP
  Migration to VoIP / SIP
  Try to avoid ‘local’ VoIP servers
  But consider emergency call out
  USE QoS
rm.com/seminars

## Slide 23: Quality of Service – Demonstration
rm.com/seminars

## Slide 24: What is QoS & How does it work?
Version
Hdr
Length
DSCP
IPv4 Packet Structure:
ECN
Header Checksum
Total Length
Fragment Offset
8-11
0-3
4-7
Identification
Flags
Time to Live
Protocol
Source IP address
Destination IP address
Options
Payload (Data – ICMP / UDP / TCP packet)
12-15
16-19
20 …
rm.com/seminars

## Slide 25: What is QoS & How does it work?
DSCP
Differentiated Services Code Point
Replacement for ”Class of Service” (CoS)
6 bit field (64 values) used to mark packets
Used to determine which packet queue to place a packet in:
Expediting Forwarding (46)
Assured Forwarding:
Low Drop AF31(26)
Medium / High Drop AF32 (28)
Best Effort (0)
Less than Best Effort CS1 (8)
Network Control
Assured Forwarding:
Low Drop AF21 (18)
Medium Drop AF22 (20)
Routing Protocols (e.g. BGP)
Voice & Video Realtime Data
Voice & Video Control / setup
Priority Applications
Web Browsing / YouTube
Low priority – e.g. backup traffic
rm.com/seminars

## Slide 26: What is QoS & How does it work?
Packet Queues
Assigned different ‘bandwidths’
  Some fixed (can’t exceed)
  Some flexible – (can exceed if spare available)
Network Interface with Known Bandwidth Limit
High Priority (EF)
Assured Forewarding
Network Control
Best Effort
Get first ‘dibs’
But have maximum set
Lower priority
But allowed to ‘burst’
rm.com/seminars

## Slide 27: Security - Firewalls
Local | Cloud
Hardware maintenance & replacement costs | Limited Feature-set
Complexity of rule sets | Reliance on someone else
True High Availability (HA) is hard | 
Local | Cloud
Full feature set | High Availability
Speed of Management | Ruleset simplification
 | Monitoring & Upgrades are Somebody Else’s Problem
rm.com/seminars

## Slide 28: Inter-site Connectivity
School Clusters
Single Administrative Domain
LA Level, MAT & Shared IT Groups
Needs to connect:
Telcos
Technology Types
Options to think about:
Any-to-Any
Node & Spoke
Encryption
rm.com/seminars

## Slide 29: Virtual Private Networks
rm.com/seminars

## Slide 30: Part 2: Summary & Recommendations
Voice Needs QoS!
Firewalls – Balance of flexibility & management
Flexible Inter-site Connections
VPNs to enable cloud migration
rm.com/seminars

## Slide 31: Questions
rm.com/seminars